## Slide 1
Determining the root causes of problems for complex electromechanical systems is difficult. Systems can detect fault states quite reliably using simulated software models; however, even when a fault is detected, it can be difficult to determine the underlying reasons, and resolution method, for that fault. Some anticipated faults may be automatically recovered from, but others are more complex and require humans to understand their root causes before resolving them.
PROBLEM
MOTIVATION
We incorporated many different ideas from the fields of data visualization, and examined historical tools and theories for ideas. In this section, we give descriptions and justifications of components we implemented.
Fault Monitoring Window
Borrowing from traditional monitoring interfaces, this part of the visualization has a traditional live data display panel, including the current system time and values of specified telemetry channels. Which channels’ values are shown is configurable.
This window also carries a description of any recent faults, along with details of the rules that originally caused them to trigger, and any other additional fault-related notes that system designers or operators have included for reference. This additional information, uncommon in traditional fault monitoring system, accelerates the fault diagnosis problem by immediately pointing towards possible root causes.
Finally, an LED-shaped icon shows the current fault state, in order to quickly grab the attention of the operator.
Channel Hierarchy Window
A degree-of-interest tree displays the hierarchy of all of the data channels. Major systems are broken into subsystems, which are then again broken into smaller subsystems, until the channels are reached at the leaf nodes. Clicking allows for expansion and navigation of the tree, and allows channel data to be selectively added to the Plotting Window. When a fault occurs, any related nodes on the tree are flagged, and those flags are propagated upwards to allow an operator to trace through the tree to find the channels affected by faults.
Plotting Window
This component provides a set of configurable plots of live telemetry channel data. The plots update as new data comes in over the network. This component is tightly linked to the Channel Hierarchy Window, which provides an interface for adding new channels to be displayed. When a fault occurs, the channels determined to be most relevant to that fault are shown. Even in a fail-safe mode where no new telemetry is being received, the plot display allows a human operator to review data leading up to the fault.
Global Correlation Matrix
This 2D matrix shows Pearson Correlation Coefficients across many different data channels, based on the most recent telemetry channel values. These cross-correlations are visualized using hue to show positive/negative correlation, and intensity to show the strength of that correlation. With this widget, an operator can see correlations of channel changes, suggesting possible interconnectedness or causation.
APPROACH
RESULTS
CONCLUSIONS
REFERENCES
ACKNOWLEDGEMENTS
The fault diagnosis process is very difficult, and can take weeks to months. It involves intense scrutiny of potentially thousands of data channels, and often the only comprehensive understanding of how these data channels relate to each other is encoded in human “tribal knowledge.” For this reason, a large amount of domain expertise is required to even begin this process.
Because diagnosing the root cause of system faults can take thousands of man-hours of expert time, any tools that can facilitate the navigation and organization of this task can potentially save a lot of money and time. However, visualizations designed for telemetry monitoring and fault diagnosis encounter the following major issues:
Displaying data from thousands of different channels isn’t practical
It’s unclear how best to organize thousands of different interrelated channels to make interesting ones findable
We’d like to have automatic discovery and visualization of relationships between channels
The tools ought to be able show many views of data in a coherent interface
Modern research has made some headway
University of Washington, Computer Science & Engineering/Aeronautics & Astronautics
Nicholas Reiter and Nathaniel Guy
Better Tools for Fault Diagnosis in Complex Systems
APPROACH (cont.)
Channel Correlation Vector
This component is similar to the Global Correlation Matrix, but shows channel correlations for a specific channel under review. The names of correlated channels are displayed for quick reference and faster lookup than the Global Correlation Matrix could provide.
Additional Features
We implemented a number of additional changes to the application that differentiate it from traditional telemetry monitoring interfaces and improve its applicability to a wide variety of systems and problems:
Channel hierarchy and fault definitions are easily configurable via .json files
Data server performs automatic fault detection based on configurable rules
Data server supports multiple simultaneous connections from clients
Telemetry can be simulated based on channels means and standard deviations
Support for multiple telemetry sources, including serial input, via highly modular components
Reconfigurable telemetry deserialization format